## Slide 1: ECE6217 Lab 2: Current Mirror Circuit
09/12/2022
TA: You Zhou
E-mail: yzhou57@gwu.edu

## Slide 2
(IEEE Press Series on Microelectronic Systems) R. Jacob Baker - CMOS_ Circuit Design, Layout, and Simulation -Wiley-IEEE Press (2010) (1)

## Slide 3: Create a new Library for ECE6217
Go to Library manager window
From the menu, select File ->New ->Library
You will see a dialog like this
NAME: ECE6217_lab
Attach to existing tech library” section,
select: AMI 0.60u C5N (3M, 2P, high-res)
Press OK
Ensure no errors

## Slide 4: Create a New design
From the Library Manager, click on the “ECE6217_lab” library you just created.
From the menu, choose File->New->Cellview, and fill in the form as shown below.
In the cell Field, type “Current_mirror”
Click always when you see “Upgrade License”

## Slide 5: Instancing parts to create the Current Mirror circuit
From the Menu choose: Create -> Instance
Choose “nmos4”
The default size for this “nmos” is
W/L = 1.5um/0.6um
Then create another nmos with the
same parameters

## Slide 6: Build mirror current circuit
From the instance menu, choose “gnd” and place it under the the transistors.
Adding I/O Pins, press P to add “Vin” and “Vout” as input signal and output signal.
Then connect the Pins and electronic components with wires.

## Slide 7: Build mirror current circuit
Click check and save after you build this circuit to see if there are any errors.

## Slide 8: Make a symbol
Create -> Cellview -> From Cellview

## Slide 9: Create a Testbench
In the Library Manager, click on your “ECE6217_lab” Library.
• From the Library Manager Menu choose: File-> New-> Cellview...
• Fill it as shown below, to create a new cell called: current_mirror_tb
Click Ok. A new Composer-Schematic window appears.
Create -> Instance:
Vdd X2
vdc: 5V DC voltage X2
res: 1 K ohm
gnd
Create -> ECE6217_lab -> current mirror
Connect the power source component with the current mirror circuit
Save and check if there are any errors

## Slide 10: Testbench

## Slide 11: Simulation
Launch ->ADE L
In the Simulation window, select Setup -> Simulator/Directory/Host
Ensure the Simulator cyclic field is reading Spectre. Leave other fields to default.
In the simulation window, select Setup -> Model Libraries…
Ensure that the files shown below are in the list, if not, browse for the following files using the <…> icon

## Slide 12: Choosing Analyses
From the menu choose Analysis -> Choose...
The form appears.
Select the “trans” analysis or “dc”
Set stop time = 150u as shown in the figure

## Slide 13: Choose the simulation node
Outputs -> to be plotted ->from schematic
Click on the nodes as shown below.(do not choose wire)

## Slide 14: Run simulation

## Slide 15: Assignment
Finish the Layout of current mirror circuit
Change the width (w) of the nmos close to the output Pin from 1.5 um to 3 um and see what will happen.